New SKINTOP® BRUSH ADD-ON

Innovative counter nut with 360 degree shielding

Stuttgart, April 26, 2012

A plastic cable entry with 360 degree EMC shielding: What at first sounds like a contradiction is now becoming reality, thanks to an unconventional idea from Lapp. Instead of a brass cable gland, now all that is needed is a brass counter nut with active screen contact. A normal plastic gland can be used as a cable entry in the control cabinet. Product manager Andreas Bauer: "In a way, we put the cart before the horse and asked why the shield contact always has to be at the front in the gland." The idea for the new SKINTOP® BRUSH ADD-ON was born. Stuttgart's Lapp Group will present the patented innovation for the first time in public at the Hanover Fair (hall 11, stand C03).

Unlike in a normal brass cable gland, the highly flexible brass braids for the shielding are integrated into the much smaller counter nut. The new SKINTOP® BRUSH ADD-ON is suitable for through-holes and offers many advantages: It can be removed at any time, can be fixed with a SKINTOP® plastic gland, is lighter, simpler and more flexible. In addition the customer does not have to order an extra brass gland, but can use a plastic gland instead, which they will generally have in stock. For reliable 360 degree shielding, the space-saving SKINTOP® BRUSH ADD-ON counter nut is absolutely sufficient.

A plastic cable entry with 360 degree EMC shielding: the new SKINTOP® BRUSH ADD-ON

Text and image available for download at www.lappkabel.com/news

About the Lapp Group:

Headquartered in Stuttgart, Germany, the Lapp Group is a leading supplier of integrated wire, cabling and connector products and solutions. Its offering includes electrical and fibre optic cables, industrial plug-in and screw connectors, cabling solutions, automation technology and technical accessories. Lapp Group’s core markets are in the mechanical and plant engineering and electronics manufacturing sectors, with rapid market expansion in the renewable energy, mobility and life science industries.

Lapp Group has remained in continuous family ownership since it was founded in 1959. In the 2010/11 financial year, it recorded total consolidated sales of 847 million euros. It employs some 3,000 people, operates 15 production sites and 41 sales companies and cooperates with approximately100 national partners worldwide.